## Slide 1: Real Steel 鋼鐵擂台
Embedded System Lab (Fall 2016)
Chien-Sheng Wu 吳建昇, Yuan-Ting Hsieh 謝沅廷

## Slide 3: System Block Diagram
Player 1
Player 2
Qt GUI
BlueTooth
BlueTooth
I2C
I2C
I2C
I2C
Socket

## Slide 4: Device

## Slide 5: Raspberry Pi & MPU6050
PiBits, Clone from https://github.com/richardghirst/PiBits
I2C connect address: 0x68
YAWPITCHROLL (angle) and REALACCEL (acceleration without gravity)
  Thresthold setting by human learning
    Pitch angle between (-15~+15), Roll angle edge -45
    Acceleration change
De-bounce Setting

## Slide 6: Raspberry Pi & Raspberry Pi
Bluetooth Serial Port Profile (SPP) server and client
Left hand (Client) & Right hand (Server)
  Client:
    set rfcomm socket
    Search for remote RFCOMM port
    Connect SPP-server
  Server:
    Set Bt-dongle Class: 0x1f00
    Set SPP_SPEC (SDP Interoperability Requirements)
    Wait for RFCOMM connection
Bluetoothctl: pair two devices
Problems: Library Linking Failed? Bluetooth Block?

## Slide 7: Raspberry Pi & Qt GUI
TCP server (Qt GUI) and Client (Raspberry Pi)
QT TCP Server
Pi TCP Client
Problem: Qt Bluetooth? Dhcp Stop?

## Slide 8: Deployment Setting
$ sudo vim /etc/rc.local
Add your script before exit(0)
Default run as root
If your command runs continuously, you must be sure to fork the process by adding “&” to the end of the command
Be sure to reference absolute filenames
For example:
  /home/pi/ESL/Pi/MPU6050-right-user2/demo_dmp &
Problems: Network Setting Failed? Dhcp Delay? Rpi 2?

## Slide 9: Use Qt and QML for a GUI program
QML for fast GUI design
Combine QML and Qt – Signal Binding
Deploy a Qt program

## Slide 10: QML for fast GUI design
Auto-scaling provides by V-Play game engine
QML components tree
Signals and Handlers
State and Transitions
Multimedia (Audio and Video)

## Slide 11: Auto-scaling provides by V-Play game engine
V-Play game engine define several components to provide with auto-scaling of multiple resolutions

## Slide 12: QML Components Tree
Tree Structure:
Rectangle
  Image
  Text
Parent can modify child’s property
Siblings can access other using “id”
Child can call parent

## Slide 13: Signals and Handlers
User-defined signals and handlers
Child can call parent’s signal
Parent have it’s handler

## Slide 14: State and Transitions
Define states of components

## Slide 15: State and Transitions
Define states of components
Add transitions between each state (Some animation)

## Slide 16: State and Transitions
Define states of components
Add transitions between each state (Some animation)
Qt creator can view several states of component

## Slide 17: Multimedia
Component: Audio, SoundEffect, Video
Method: play, paused
Check file encoding for different platforms
For windows 10:
  Audio: mp3, wav
  SoundEffect: wav
  Video: wmv

## Slide 18: Use Qt and QML for a GUI program
Qt for cross-device communication
QML for fast GUI design
Combine QML and Qt – Signal Binding
Deploy a Qt program

## Slide 19: Combine QML and Qt – Signal Binding

## Slide 20: Combine QML and Qt – Signal Binding

## Slide 21: Deploy a Qt program
A deploy program is just binary with those libraries
Windows: use windeployqt that comes with qt installer
  Caution: After running this program, you need to manually copied the qml folder from original release folder
Linux: use linuxdeployqt as specified in Qt official documents

## Slide 22: Github
Git clone https://github.com/YuanTingHsieh/ESL

## Slide 23: Demo Video